## Slide 1
MONOCOPTER
Single-Blade Rotary-Wing UAV with Autonomous Stabilization
ESP32 + MPU6050 | Phase-Locked Cyclic Control
Siddhant Satote • Sanika Nikumbh Department of Electronics & Telecommunication Alard College of Engineering & Management, Pune
GUIDE Prof. Dalvi Sir
Academic Year 2026–27

## Slide 2
INTRO-
DUCTION
What is a Monocopter?
Inspired by the maple seed (samara), a monocopter achieves flight using a single rotating wing — the entire airframe spins as one unit.
🍁
Bio-Inspired Design
Rooted in autorotation & gyroscopic dynamics of samaras
⚙️
Single Motor Architecture
One BLDC motor — drastically fewer failure points vs quadcopters
🎯
Core Challenge
Phase-locked cyclic control — servo must fire at exact rotational phase
📡
Applications
Recon, emergency drops, indoor exploration, payload delivery

## Slide 3
SYSTEM ARCHITECTURE
POWER
3S LiPo 11.1V
1300–2200mAh
SENSING
MPU6050 IMU
6-DOF @ 50Hz I2C
COMPUTE
ESP32 240MHz
PID + Phase Track
ACTUATION
BLDC Motor + ESC
9g Servo Cyclic Pitch
CONTROL LOOP (50 Hz Fixed-Frequency)
① IMU Data
Acquisition
② Attitude
Estimation
③ Phase
Tracking
④ PID
Computation
⑤ Phase
Match?
⑥ Servo
Actuation

## Slide 4
HARDWARE IMPLEMENTATION
ESP32 Dev Board
Flight Controller
240MHz Dual-Core
WiFi / Bluetooth
MPU6050 IMU
Attitude Sensing
6-DOF MEMS
50Hz, I2C 400kHz
Brushless Motor
Primary Lift / Rotation
BLDC, KV TBD
3-Phase AC
ESC
Motor Speed Control
20–30A PWM Input
Throttle Control
9g Micro Servo
Phase-Gated Correction
PWM Actuation
Cyclic Pitch Control
3S LiPo Battery
Power Supply
11.1V, 1300–2200mAh
Main Power Source

## Slide 5
PHASE-LOCKED CYCLIC CONTROL
01
The Core Problem
Since the entire airframe rotates, a fixed correction command changes direction each revolution. Control must be phase-aware.
02
Phase Tracking
Gyro yaw rate is integrated each 50Hz tick to accumulate rotation angle (0°–360°).
03
PID Output → Direction
Roll + Pitch error determines the target actuation angle. 90° phase lead is added to compensate for gyroscopic lag.
04
Servo Pulse
When current phase = θ_target + 90°, servo fires a cyclic pitch pulse — once per revolution.
FIRMWARE MODULES
IMU Driver
I2C, DMP init
Attitude Est.
98% gyro + 2% accel
Phase Tracker
ωz integration
PID Controller
Roll + Pitch error
Servo Driver
Phase-gated PWM
ESC Driver
Throttle PWM
WebSocket
Live telemetry

## Slide 6
RESULTS & FUTURE SCOPE
50Hz
IMU data rate
via I2C
<5ms
Phase tracking
latency
2–3 rev
Disturbance
recovery
98/2
Gyro/Accel
filter ratio
KEY OBSERVATIONS
✓ Phase-locked cyclic control validated in tethered bench testing
✓ 90° gyroscopic phase lead correctly compensates precession lag
✓ Complementary filter tuned to 98% gyro weight to reduce vibration noise
✓ ESP32 dual-core: control loop + telemetry run concurrently
FUTURE SCOPE
🚁 Free Flight Testing
📍 GPS + Barometric Altitude Hold
🤖 AI Route Optimization
📦 Payload Bay for Drop Missions
🔗 Nexus TVC Firmware Integration
Alard College of Engineering & Management | ENTC Dept | AY 2026–27